## Slide 1: Stenosis Surgical Guidance Tool
Update – 12/8/2022

## Slide 2
Construct LPN models
Pipeline Overview
Tune BC using Surrogate
Manually Compare w/ 3D Simulation to ensure quality
Healthy: Generate Artificial Stenosis
Diseased: Detect Stenosis
Parametrize stenosis
Run LPN & train NN

## Slide 3: BC Tuning (Healthy Only) - Old
Yang et. al. 2019 Surrogate model (Modified)
Solver-determined RCL values.
Tunable RCR boundary conditions for LPA and RPA, with constant capillary wedge pressure of 7 mmHg
RPA/LPA resistances computed using resistances in series and parallel
Notes: We take a modified surrogate tuning model used by Weiguang in 2019.
We use solver computed RCL values for the MPA, and represent the RPA/LPA trees by a resistance computed using resistances in series and parallel
For actual tunable parameters, we set RCR boundary conditions for the RPA and LPA respectfully with a target capillary wedge pressure of 7

## Slide 4: Generic BC Tuning - New
Yang et. al. 2019 Surrogate model (Modified)
Solver-determined RCL values.
Tunable C/R boundary conditions – insufficient target values (4), causing optimization to be non-identifiable. We split R value into Rp:Rd using a 1:4 ratio (is this reasonable?).
RPA/LPA resistances computed differently (* Mentioned on next slide).
Targets
mPAP
sysPAP
diaPAP
Flow Split
Notes: We take a modified surrogate tuning model used by Weiguang in 2019.
We use solver computed RCL values for the MPA, and represent the RPA/LPA trees by a resistance computed using resistances in series and parallel
For actual tunable parameters, we set RCR boundary conditions for the RPA and LPA respectfully with a target capillary wedge pressure of 7

## Slide 5: Difference in computing LPA & RPA R
Resistances in Series & Parallel
  Only gives approximate pressure drops of .3 mmHg (healthy) and .75 mmHg (diseased)
  Poor approximation, since we would expect > 1 at minimum.
  Use as starting point (is there a better approx. for the start? Ex. Splitting the computed PVR & capacitance used as optimization IC.)
Average of LPA outlets and RPA outlets & (Q = /R)
  Healthy: Approx. 1.16 mmHg for both sides
  Diseased: 1.6 mmHg for RPA & 8.4 mmHg for LPA
  Better approximation, but requires a full 0D simulation to be run.

## Slide 6: Diseased Model Bottleneck
Trying to use Ingrid’s AS1_SU0308 model
Some silly issues that would not occur in practice due to physiological measurements.
Solved Problems
  Reconstructing a model from the XMT format. (issues with a branch not connected properly)
  Adequate centerline generation for segmentation

## Slide 7: Main Problem – 3D simulation fails to stabilize

## Slide 8: Mesh Quality
  Refined & double checked, so this should not be an issue
  Worst Qualities 

## Slide 9: Inflow BC
Ingrid’s models do not come with physiological inflows, so they were tuned
2 Versions, neither matching physiological values well.
CO = 5.83
Pressure: (90, 18, 42)
Tried scaling Version 2 to match, but problems in BC tuning
Version 1: Matches CO (5.77), but not pressure targets (122 mmHg)
Version 2: Pressure targets (93 mmHg), but not CO (5.2 ml/s)
Scaled Plots ->

## Slide 10: Outflow BC tuning
Version 2 inflow tunes to 0 capacitance, even when scaled to correct CO
Version 1 with different configurations:
  No scaling to CO (minor difference anyways)
    Tunes to capacitances of 1e-10, which causes RC constant to be extremely small, which could affect convergence
    Tried replacing all capacitances with 1e-6 to test, but failed faster.
  Small scaling to CO only
    Tunes to 0 capacitance
  Scaling & changing diaPAP to 20
    Is it even possible to get < 20 minPAP if the PCWP = 20 mmHg?
    Tunes to ~1e-6 or 1e-7 capacitance
    Simulation runs for longer, but still fails.
    Also values for log of residual change are worse.

## Slide 11: Next Steps after Bottleneck
Comparing 3D and 0D models to ensure they are close or at least correlated.
Detecting/Parametrizing Stenosis in diseased model
Training model for diseased model (should not be problematic).